## Slide 1: Hardware Maintenance Training

## Slide 3
• Laser Output: | 10 Watt
• Type : | CO2 Laser
• Laser Classification: | Class I
• Spot Size: | 0.003
• Input AC Voltage: | 110/220VAC50/60Hz
• Current: | 4 Amps
• Dimensions: | 6”x15”x20”
• Weight: | 30 lbs.
SPECIFICATIONS

## Slide 4: Preventative Maintenance Schedule
1. Clean Final Lens Monthly
2. Clean Galvanometer Mirror Monthly
3. Clean Exhaust Fan Monthly
4. Check/Clean Beam Expander Optics Monthly
5. Check / Clean / Lube Drive Assembly Monthly

## Slide 5: Required Tools:

## Slide 6: Required Tools:
1. Allen Wrench Set (English)

## Slide 7: Required Tools:
Allen Wrench Set (English)
Lint Free Cloth

## Slide 8: Required Tools:
Allen Wrench Set (English)
Lint Free Cloth
White Vinegar

## Slide 9: Required Tools:
Allen Wrench Set (English)
Lint Free Cloth
White Vinegar
SAFETY GLASSES!

## Slide 10: DISASSEMBLY

## Slide 11
Remove Power / Cables Remove Four Screws
BEFORE BEGINNING MAKE SURE POWER IS TURNED OFF

## Slide 12
Manually Retract Drawer Slide Cover Off From Top

## Slide 13: Monthly Preventative Maintenance

## Slide 14
Clean/Dust Drive Mechanism
Clean Fan and Air Paths
Clean Drawer Guides

## Slide 15
Inspect / Clean Final Lens Inspect / Clean Mirror
DO NOT Rotate Mirror by Hand

## Slide 16
Clean Final Lens

## Slide 17
Inspect / Clean and Confirm Cooling and Exhaust Fan

## Slide 18
Dust 30VDC and Control Board

## Slide 19: Optics Training and Cleaning

## Slide 20
Optical Beam Path

## Slide 22
When Cleaning Optics:
  Make sure the lens or mirror is very wet with vinegar.
  Lens and mirrors are surface coated and
  are very easy to scratch.
  Dab or lift the dust and vinegar off the surface.
  Never rub or polish the surface.
  Never use air to dust around lens or mirrors.
  When Inspecting surfaces, look for scratches or burns
  Replace scratched or burned mirror or lens.

## Slide 23
DO NOT USE FORCED AIR DUSTERS
THEY CAN DAMAGE OPTICS
X

## Slide 24
Thank You
        Field Service: 1-800-401-0716 (Domestic)
        1-740-642-4666 (International)
        InfoSight : 1-740-642-3600
        Forum : http://www.infosight.com/forums/
Online Manual: http://www.infosight.com/download/pdf/manuals/jm410.pdf