## Slide 1
Hardware Maintenance Training

## Slide 2
Specifications
Laser Output: |  | 30 Watt
Type: |  | CO2 Laser
Laser Classification: |  | Class I
Spot Size: |  | .003
Input AC Voltage: |  | 110/220 VAC 50/60Hz
Current: |  | 10 Amps
Dimension: |  | 9” X 8” X21”
Weight: |  | 21 Lbs

## Slide 3
Preventative Maintenance Schedule for LL3036

## Slide 4
Required Tools:

## Slide 5
Required Tools:
Security Torx driver – T25

## Slide 6
Required Tools:
Security Torx driver – T25
Allen wrench set (English)

## Slide 7
Required Tools:
Security Torx driver – T25
Allen wrench set (English)
Lint free cloth

## Slide 8
Required Tools:
Security Torx driver – T25
Allen wrench set (English)
Lint free cloth
White vinegar

## Slide 9
Required Tools:
Security Torx driver – T25
Allen wrench set (English)
Lint free cloth
White vinegar
S A F E T Y G L A S S E S ! ! ! !

## Slide 10
Preventative Maintenance Schedule for LL3036

## Slide 11
Weekly Preventative Maintenance

## Slide 12
Air Filter – Remove – Inspect - Clean - Replace
Remove thumbs screws Remove filter media

## Slide 13
Inspect exhaust - Clean

## Slide 14
Inspect pass through lens – Clean if necessary

## Slide 15
Preventative Maintenance Schedule for LL3036

## Slide 16
Disassembly

## Slide 17
Remove power cables Remove allen screws

## Slide 18
Remove pass through Remove bottom torx screws

## Slide 19
Remove rear torx Remove tag spool and shaft

## Slide 20
Remove case

## Slide 21
Monthly Preventative Maintenance

## Slide 22
Preventative Maintenance Schedule for LL3036

## Slide 23
Clean fan and air paths
Clean/Dust drive mechanism
Clean top and bottom drive rollers

## Slide 24
Remove galvo mirror mover Inspect / Clean mirror

## Slide 25
Clean final lens

## Slide 26
Inspect / Clean and confirm cooling and exhaust fans

## Slide 27
Dust 30VDC and control board

## Slide 28
Check pulley lock screws
Inspect drive belts for wear

## Slide 29
Check and clean
Notch and tag sensors

## Slide 30
Optics Training and Cleaning

## Slide 31
Remove optics cover

## Slide 34
Optical beam path

## Slide 36
When cleaning optics ,
Make sure the lens or mirror is very wet with vinegar.
Lens and mirrors are surface coated and
are very easy to scratch.
Dob or lift the dust and vinegar off the surface.
Never rub or polish the surface.
Never use air to dust around lens or mirrors.
When inspecting surfaces, look for scratches or burns
Replace and scratched or burned mirror or lens.

## Slide 37
DO NOT USE FORCED AIR DUSTERS
THEY CAN DAMAGE OPTICS
X

## Slide 38
LL3036 Trouble Shooting Chart

## Slide 39
Thank You
Field Service: 1-800-401-0716
InfoSight : 1-740-642-3600
Forum : http://www.infosight.com/forums/
Online Manual: http://bit.ly/28YBaLT