## Slide 1: Hardware Maintenance Training

## Slide 2
Training for LL4000 Series
of metal tag printers.
60/80/100 Watt Laser
Water cooled

## Slide 3
SPECIFICATIONS
• Laser Output: | 60-100 Watt
• Type : | CO2 Laser
• Laser Classification: | Class I
• Spot Size: | .006
• Input AC Voltage: | 110/220VAC50/60Hz
• Current: | < 15 Amps
• Dimensions: | 15”x16”x30”
• Weight: | <100 lbs.

## Slide 5
Required Tools:

## Slide 6: Required Tools:
1. Allen Wrench Set (English)

## Slide 7: Required Tools:
Allen Wrench Set (English)
Lint Free Cloth

## Slide 8: Required Tools:
Allen Wrench Set (English)
Lint Free Cloth
White Vinegar

## Slide 9: Required Tools:
Allen Wrench Set (English)
Lint Free Cloth
White Vinegar
SAFETY GLASSES!

## Slide 11
Weekly Preventative Maintenance

## Slide 12
Inspect Pass Through Lens – Clean if Necessary

## Slide 14
Disassembly

## Slide 15
Remove Power / Cables Remove 18 Allen Screws
BEFORE BEGINNING MAKE SURE POWER IS TURNED OFF

## Slide 16
Remove pass through

## Slide 17
Remove Slide Cover

## Slide 18
Monthly
Preventative Maintenance

## Slide 20
Clean fan and air paths
Clean/Dust drive mechanism
Clean top and bottom drive rollers

## Slide 21
Remove Galvo mirror cover
Inspect / Clean mirror
Clean Final Lens

## Slide 22
Inspect / Clean filter and confirm cooling and exhaust fans

## Slide 23
www.infosight.com 740-642-3600
Dust Power supply and 30VDC and Control Board

## Slide 24
Check pulley lock screws
Inspect drive belts for wear

## Slide 25
Check and clean
notch and tag sensors

## Slide 26
Optics Training and Cleaning

## Slide 27
Remove optics cover

## Slide 30
Optical Beam Path

## Slide 32
When Cleaning optics ,
Make sure the lens or mirror is very wet with vinegar.
Lens and Mirrors are surface coated and
are very easy to scratch.
Dob or lift the dust and vinegar off the surface.
Never Rub or polish the surface.
Never use air to dust around lens or mirrors.
When Inspecting surfaces, look for scratches or burns
Replace and scratched or burned mirror or lens.

## Slide 33
DO NOT USE FORCED AIR DUSTERS
THEY CAN DAMAGE OPTICS
X

## Slide 35: Spares

## Slide 36
Thank You
Field Service: 1-800-401-0716
Infosight : 1-740-642-3600
Website: www.infosight.com
Forum : http://www.infosight.com/forums/
Online Manual: http://www.infosight.com/support/manuals/188-labelase-4000-tag-printer-manuals